## Slide 1
TEAM ANUWAD
BAIF Anuwad
Studio
Offline translation for field media
English, Hindi and Marathi
Text, audio and video
Notes: Good morning. We are Team Anuwad. Our solution is BAIF Anuwad Studio, an offline application that translates English, Hindi, and Marathi text, audio, and video. The purpose is to make BAIF field content usable in the language people understand while keeping the files and models inside BAIF infrastructure.
[Sources]
- HSBC logo reference image supplied by the user in this conversation.

## Slide 2
Problem statement
02
BAIF field content often needs to reach people who use different languages.
Content
Training videos, meeting recordings, instructions and written material
Need
Translation, voice output and captions in English, Hindi and Marathi
Constraint
On-premises operation with no normal internet, cloud API or HSBC-system dependency
The application must also handle real media formats and create outputs that users can download and share.
Notes: BAIF uses training videos, meeting recordings, instructions, and written material. Language can limit how widely this information is used. The requirement is to accept text, audio, and video, create translations and voice output, support captions, and avoid normal internet or cloud dependency during use.
[Sources]
- HSBC logo reference image supplied by the user in this conversation.

## Slide 3
Overall solution
03
BAIF Anuwad Studio gives the operator one simple workflow.
01
Upload
Text, audio or video
02
Recognise
Create a timed transcript
03
Translate
Convert to the chosen language
04
Generate
Create voice and subtitles
05
Deliver
Download text, audio and video
The system selects the local processing route automatically. The user only needs to select the languages and start the job.
Notes: The operator has one simple workflow. They upload a file or enter text, choose the source and target languages, and start translation. The application recognises speech when needed, translates the content, generates voice and subtitles, and prepares downloadable files.
[Sources]
- HSBC logo reference image supplied by the user in this conversation.

## Slide 4
Inputs and outputs
04
Input
Output
Text
Written English, Hindi or Marathi
Audio
MP3, WAV, AAC, M4A, FLAC, WMA and OGG
Video
MP4, MOV, AVI, WMV, MKV, FLV and WebM
Translated text and JSON
Continuous dubbed WAV audio
SRT subtitle file
Translated MP4 video
Optional summary
Notes: The application accepts text, common audio files such as MP3 and WAV, and common video files such as MP4, MOV, MKV, and WebM. It produces translated text, JSON, continuous dubbed audio, SRT subtitles, an optional summary, and a translated video when the input is a video.
[Sources]
- HSBC logo reference image supplied by the user in this conversation.

## Slide 5
Local processing pipeline
05
01
Media preparation
FFmpeg reads and normalises media
02
Speech recognition
Faster-Whisper creates timestamps
03
Translation
IndicTrans2 converts language
04
Voice generation
Sherpa-ONNX produces speech
05
Video export
FFmpeg creates the final file
Every stage reads local files and writes local artifacts in the BAIF workspace.
Notes: The technical workflow has five local stages. FFmpeg prepares the media. Faster-Whisper converts speech to a timestamped transcript. IndicTrans2 translates the text. Sherpa-ONNX creates the target-language voice. Finally, FFmpeg combines the translated audio and subtitles with the video. After model installation, every stage runs locally.
[Sources]
- HSBC logo reference image supplied by the user in this conversation.

## Slide 6
Speech recognition
06
Faster-Whisper
Local multilingual speech recognition with timestamps
Languages
English, Hindi and Marathi source speech
Deployment
CPU inference with INT8 processing
Timing
Timestamped segments for subtitles and video alignment
Reliability
Overlapping windows, context and repetition cleanup
Notes: For speech recognition, we selected Faster-Whisper. It supports English, Hindi, and Marathi and produces timestamps needed for subtitles and video alignment. It is configured for CPU-based INT8 processing, which is practical for the BAIF deployment machine. We also use overlapping processing windows and cleanup logic to reduce missed words and repeated segments.
[Sources]
- HSBC logo reference image supplied by the user in this conversation.

## Slide 7
Translation
07
IndicTrans2
Indian-language translation with local CTranslate2 inference
English and Indic-language routes
The corresponding local model handles English to Hindi or Marathi, and Hindi or Marathi to English.
Hindi and Marathi route
The application uses local English as an intermediate language to cover Hindi to Marathi and Marathi to Hindi.
Context control
Adjacent transcript segments are merged before translation. Repetition cleanup runs after decoding.
Notes: For translation, we use IndicTrans2 with CTranslate2 for efficient local inference. IndicTrans2 is selected because it is built for Indian languages. For English and an Indian language, the system uses the corresponding local model. For Hindi and Marathi, it uses English as a local intermediate language. This gives coverage for every required language direction without any cloud call.
[Sources]
- HSBC logo reference image supplied by the user in this conversation.

## Slide 8
Voice generation
08
Sherpa-ONNX VITS
Local English, Hindi and Marathi text-to-speech models
Continuous audio
A clean WAV file for listening and sharing, without adding artificial pauses between translated clips.
Video-timed audio
A separate WAV track aligned to source timestamps. The final video can retain space needed to match the original scenes.
Notes: For translated voice, we use Sherpa-ONNX VITS models stored locally for English, Hindi, and Marathi. The system creates continuous WAV audio for listening. It also creates a separate time-aligned version for the final video, so voice appears with the original scenes.
[Sources]
- HSBC logo reference image supplied by the user in this conversation.

## Slide 9
Captions and video export
09
SRT subtitles
Translated text and timestamps are written to a standard subtitle file.
Dubbed audio
The time-aligned voice track is prepared for the original video.
Final MP4
FFmpeg creates a ready-to-share translated video.
The operator can download the subtitle file separately or create a video with captions burned into the final MP4.
Notes: The application writes translated subtitles as an SRT file. It then uses FFmpeg to combine the original video with the translated audio. If needed, captions can be burned into the final MP4. This provides both editable subtitles and a ready-to-share translated video.
[Sources]
- HSBC logo reference image supplied by the user in this conversation.

## Slide 10
Quality and reliability
10
Skipped speech
Overlapping ASR windows, midpoint ownership and gap recovery
Repeated words
Consecutive-word and phrase-level repetition cleanup
Translation context
Adjacent transcript segments are merged before translation
Audio and video timing
Continuous download audio plus a separate video-timed audio path
Noisy recordings, unfamiliar terms and strong local dialects should still receive human review before important external use.
Notes: We focused on the visible issues users notice first: skipped speech, repeated words, translation quality, and audio timing. The pipeline uses ASR overlap and gap recovery, repetition cleanup, merged translation context, and separate continuous and video-timed audio paths. These controls improve practical output quality, although noisy speech and local dialects should still be reviewed before high-stakes use.
[Sources]
- HSBC logo reference image supplied by the user in this conversation.

## Slide 11
Offline deployment
11
Application
Python 3.12 and Streamlit
Models
Local Whisper, IndicTrans2 and TTS model vault
New-machine setup
Copy the approved model vault by pendrive, or download it once with temporary internet access.
Normal operation
Uploaded media, outputs and cache remain on BAIF infrastructure. Normal translation uses no cloud API or internet connection.
Model verification confirms that the local vault contains the required speech recognition, translation and voice models before handover.
Notes: The application uses Python, Streamlit, FFmpeg, local SQLite caching, and the approved local model vault. The model vault contains Whisper, IndicTrans2, and text-to-speech models. A new machine can receive the vault through a pendrive, or download it once using temporary internet access. Normal translation then runs without internet, HSBC systems, or cloud APIs.
[Sources]
- HSBC logo reference image supplied by the user in this conversation.

## Slide 12
Live demonstration
12
1
Upload a short media file
2
Select source and target languages
3
Start translation
4
Follow completion percentage and status
5
Review text, audio, subtitles and video
6
Repeat with internet disconnected
The interface hides technical logs and gives the end user a completion percentage with simple status messages.
Notes: For the demo, I will upload a short file, choose the source and target languages, and start processing. The interface shows a completion percentage and a plain-language message instead of technical logs. When processing finishes, I will show the translated text, dubbed audio, SRT subtitles, and final translated video. We can then disconnect internet and repeat with a new file to show that processing remains local.
[Sources]
- HSBC logo reference image supplied by the user in this conversation.

## Slide 13
Thank you
Notes: Thank you.
[Sources]
- HSBC logo reference image supplied by the user in this conversation.